## Slide 1: Aicar
for AI projects

## Slide 2: outline
About Aicar
Hardware Compents
Software Compents
Functions
Interfaces
Applications

## Slide 3: Aicar
In computer science, the field of AI research defines itself as the study of "intelligent agents": any device that perceives its environment and takes actions that maximize its chance of success at some goal.
Aicar is an inexpensive (~ 50￥) intelligent agent for carrying out research projects in artificial intelligence. With Aicar, you can test different AI algorithms and policies for conducting actions based on various sensors input.

## Slide 4: Aicar Hardware

## Slide 5: Hardware Compents
Arduino UNO
BT06 Bluetooth
HC-SR04 Ultrasonic Distance Measuring
L293D Motor Drive Shield
2WD Smart Robot Car Chassis Kit
Notes: an inexpensive two-wheeled differentially-steered robot based on the popular Arduino Uno compatible microcontrollers

## Slide 6: Software Compents
Video Capture Tools
  DroidCam for Android
  DroidCam Client for Win/Linux
Development
  Arduino IDE (C/C++)
  Matlab
  Python

## Slide 7: Functions
#include <AFMotor.h>
AF_DCMotor Rback_motor(4);
AF_DCMotor Lback_motor(1);
float RLRatio = 1.0;
int maxSpeed = 80;//最大速度
char getstr;//串口数据
int IntervalTime;//测距时间
int trig = 9;//sero1保留端口
int echo = 10;//sero2保留端口
int control=1;//0:人工控制;1:自动控制

## Slide 8: Functions
void setup() {
// put your setup code here, to run once:
Serial.begin(9600);
Rback_motor.setSpeed(0);
Rback_motor.run(RELEASE);
Lback_motor.setSpeed(0);
Lback_motor.run(RELEASE);
delay(2000);
//超声波测距
pinMode(echo, INPUT);
pinMode(trig, OUTPUT);
}

## Slide 9: Functions
void loop() {
getstr = Serial.read();
driver();
if(control==1){
ultrasonicCar();
}
}

## Slide 10: Functions
void forward() {
Rback_motor.run(BACKWARD);
Lback_motor.run(BACKWARD);
Rback_motor.setSpeed(maxSpeed*RLRatio);
Lback_motor.setSpeed(maxSpeed);
}
void backward() {
Rback_motor.run(FORWARD);
Lback_motor.run(FORWARD);
Rback_motor.setSpeed(maxSpeed*RLRatio);
Lback_motor.setSpeed(maxSpeed);
}

## Slide 11: Functions
void stopcar() {
Rback_motor.setSpeed(0);
Lback_motor.setSpeed(0);
Rback_motor.run(RELEASE);
Lback_motor.run(RELEASE);
}
void left(){
Rback_motor.run(FORWARD);
Lback_motor.run(BACKWARD);
Rback_motor.setSpeed(maxSpeed*RLRatio);
Lback_motor.setSpeed(maxSpeed);
}
void right(){
Rback_motor.run(BACKWARD);
Lback_motor.run(FORWARD);
Rback_motor.setSpeed(maxSpeed*RLRatio);
Lback_motor.setSpeed(maxSpeed);
}

## Slide 12
void driver() {
if ((getstr == '<')&&(RLRatio>0.1)) {
RLRatio -= 0.1;
Serial.println(RLRatio);
}
if (getstr == '>') {
RLRatio += 0.1;
Serial.println(RLRatio);
}
if (getstr == '5') {
Serial.println("stopcar");
stopcar();
control=0;
}
if (getstr == '1') {
Serial.println("forward");
forward();
control=0;
}
if (getstr == '2') {
Serial.println("backward");
backward();
control=0;
}
if (getstr == '3') {
Serial.println("right");
right();
control=0;
}
if (getstr == '4') {
Serial.println("left");
left();
control=0;
}
if (getstr=='6'){
control=1;
Serial.println("Auto Control On");
}
if(getstr=='7'){
control=0;
Serial.println("Auto Control Off");
}

## Slide 13
float getdistance() {
digitalWrite(trig, 1);
delayMicroseconds(15);
digitalWrite(trig, 0);
IntervalTime = pulseIn(echo, HIGH);
return IntervalTime / 58.00;
}
void ultrasonicCar() {
float s = 0;
s = getdistance();
ultrasonicCar(s);
}
void ultrasonicCar(float s) {
if ((s < 40)&&(s>0)){//40cm以内
randomright();
}else{
forward();
}
}
void randomright(){
Rback_motor.run(BACKWARD);
Lback_motor.run(FORWARD);
Rback_motor.setSpeed(maxSpeed*RLRatio);
Lback_motor.setSpeed(maxSpeed);
long n = random(50,1000);//随机转向 0.05 - 1秒
delay(n);
Rback_motor.setSpeed(0);
Lback_motor.setSpeed(0);
}

## Slide 14: Interfaces - Matlab
instrhwinfo('bluetooth')
instrhwinfo('bluetooth','BT04-A')
b=Bluetooth('BT04-A',1);
fopen(b);
fwrite(b,'101X');

## Slide 15: Interfaces - Matlab
clear;
sp=actxserver('SAPI.SpVoice');
camera=webcam(2); %connect to camera
nnet=alexnet;%load neural network alexnet
%make a circle to reload frame from camera
while true
picture=camera.snapshot;
picture=imresize(picture,[227,227]);%resize picture
picture=imrotate(picture, -90);
label=classify(nnet,picture);%
image(picture);
title(char(label));
sp.Speak(char(label));
drawnow;
end

## Slide 16: Interfaces - Python
>>> a = "AB:A4:95:56:34:02"
>>> sock = bluetooth.BluetoothSocket(bluetooth.RFCOMM)
>>> sock.connect((a,1))
>>> sock.send(“1")
>>> data = sock.recv(12)
>>> print 'received [%s]'%data
>>> sock.close()

## Slide 17: Interfaces - Python
vid= cv2.VideoCapture(0)
time.sleep(2)
b=vid.read()[1]
cv2.namedWindow("a")
cv2.imshow("a",b)
cv2.waitKey(0)
cv2.destroyAllWindows()

## Slide 18: Applications
Video demo …

## Slide 19: References
Arduino.cc — Introduce microcontroller used in this project, get project ideas, and learn programming tips, Arduino is a very popular and relatively inexpensive way to do projects with microcontrollers. 
Taobao.com — All stuff used, including Arduino Uno, DC motors, sensors and more. A corresponding components reference list for the Aicar hardware is attached.

## Slide 20: Aicar components list
For reference only

## Slide 30
Notes: power bank (充电宝) is preferred.